## Slide 1: Serum calcium measurement

## Slide 2: Serum Calcium
Calcium is an essential mineral.
In the plasma, it is present in three forms:
• Free ionized (Ca++)
• Protein‐bound (principally to albumin)
• Complexed (primarily with phosphate and citrate).

## Slide 3: Calcium Functions
• The control of ion transport across cell membranes (particularly relevant to excitable tissues)
• Acting as an intracellular second messenger
• Activation of blood coagulation factors, coupling neuromuscular excitation and providing the strength and rigidity of bones and teeth.

## Slide 4: Estimation of calcium
Principles :
Colorimetric determination of calcium without deproteinization using O-cresol phthalein complex. Interference due to Mg+2 is eliminated by B-hydroxyquinoline (up to 4mmol/L, 0.01mg/L).

## Slide 5
Procedure:
 | blank | Standard | Sample
Sample | ………… | …………. | 20microliter
Reagent 1 (Std) | …………. | 20microliter | ………….
Working solution (R2+R3) | 1 mL | 1mL | 1mL
Mix, read absorbance after 5minutes at 572nm against blank . The color intensity is stable for 1hr .

## Slide 6: Inorganic phosphorus
Blood phosphorus Present in the blood can be classified as :
1-Inorganic phosphorus , like phosphate
2-Organic phosphorus like glycerophosphates, nucleotide phosphate, hexosephosphate .
3-Lipid phosphorus like lecithin, cephalin.

## Slide 7
Phosphorus is a major intracellular anion in mammals, Total body phosphorus in a 70-kg man is about 700 to 800 mg, 85% of which is in the skeleton in hydroxyapatite phase; the remaining 15% is in soft tissues.
The majority of the phosphate in the body is in the organic form as a complex with carbohydrates, lipids, and proteins.
Phosphorus is an essential element in the cellular structure, cytoplasm, and mitochondria.
The normal serum phosphorus concentration is 3.4 to 4.5 mg/dl (1.12 to 1.45 mmol/L). This fluctuates with age (it is higher in children than adults), dietary intake, and acid–base status. There is a diurnal variation, which reaches its nadir between 8 and 11 a.m.

## Slide 8
Fasting is required before doing the test because phosphorus enter red blood cell with glucose
there is difference between levels in the blood from that in the serum or plasma (whole blood contain higher than plasma or serum ) the differences result from that the RBC richer in phosphorus than in plasma mainly because they contain more ester phosphate so it is important to avoid hemolysis of blood samples.

## Slide 9: Determination of Inorganic phosphorus
Principles :
Colorimetric determination , without deproteinization of serum phosphorus using a single reagents which forms a phosphomolybdate complex in the presence of reducing agents (ferrous sulphate).

## Slide 10
Procedure:
 | Blank | Standard | Sample
Sample | ……. | …….. | 100microliter
Reagent (std) (5mg/dL,1.61mmole/L) |  | 100microliter | ……
D.W | 100microliter | ….... | …...
Working solution (R2+R3) | 2.5mL | 2.5mL | 2.5mL
Mix and wait 10min , measure the absorbance of sample and standard at 690nm.